# Text boxes

| TAXI |
| --- |
| Parking Brake | released |
| Brakes | CKD |
| Turning Instruments | CKD |

| AFTER START |
| --- |
| Cowl Flaps | UP |
| Avionic Master Switch | ON/SET |
| Transponder | SbY/ GND |
| NDB/NAV/etc | ON/SET |
| Board-Radio-Paxe | ON |

| START UP |
| --- |
| Primer | AS REQUIRED/LOCK |
| Carburetor Head | COLD |
| Throttle | OPEN / 8 mm |
| Proplever | HIGH RPM |
| MIXTURE | RICH |
| BEACON | ON |
| Outside Area | CLEAR |
| Ignition Switch | START |
| Throttle | 1200 RPM |
| Oil Pressure | CKD |
| Generator | CKD |
| Suction | CKD |

| COCKPIT |
| --- |
| Flight Preparation | COMPLETED |
| Weight & Balance | CKD |
| Airplane Documents | GKD/on Board |
| Fuel Quantity | ……HRS,……MIN |
| Seats & Belts | ADJUSTED/LOCKED |
| Cabin Doors | LATCHED |
| Parking Brake | SET |
| Avionic Master Switch | OFF |
| /AP/Transponder | OFF |
| Electrical Switches | OFF |
| Circuit Breakers | IN |
| Cowl Flaps | OPEN |
| Fuel Valve | BOTH |
| Master Switch | ON |
| Alternate Air | CLOSED |

| Normal Checklist 182 Front | D-EDJW | EDAN | 02/12 |
| --- | --- | --- | --- |

| RUN UP |
| --- |
| Parking Brake | SET |
| Engine Instruments | GREEN-RANGE |
| Throttle | 1700 RPM |
| Generator | CKD |
| Suction | green |
| Magnetos | 125/50 CKD |
| Prop Control | CKD |
| Carburetor Heat | CKD |
| Throttle | 1200 RPM |

| TAKE OFF |
| --- |
| Directional Gyro | CONFIRM |
| Landing/Taxi/Strobe Light | ON |
| Transponder | ON/ALT |
| T/O Power | full throttle / 2600 RPM |
| rotate | 60 MPH |

| INITIAL APPROACH/DESCENT |
| --- |
| Altimeter | hPa /CKD |
| Directional Gyro | SET |
| Carb. Heat | AS REQUIRED |
| Mixture | ENRICH |
| Cowl Flaps | CLOSED |

| Cruise Performance 65% BHP |
| --- |
| NIK TANK (200 l) MAX. WT / STANDART ATMOSPHERE MIXTURE LEAN |
| ALT (PA in ft.) | 2000 | 5000 | 7500 |
| MP (in./ Hg.) | 22 | 21 | 21 |
| RPM | 2300 | 2300 | 2300 |
| FF (USGal/h)*) | 13,4 | 13,1 | 13,4 |
| TAS (MPH) | 149 | 151 | 156 |
| % BHP | 67 | 64 | 66 |
| FF (I/h) | 50,8 | 49,5 | 50,8 |
| Safe Endurance (Empty Tank) | 3:56 | 4:02 | 3:56 |
| TAS (KTS) | 130 | 131 | 136 |

*) 10 % Contingency included

Safe Endurance =

Fuel usable / (FF + 10 % Cont.) – 30 MIN.

| LEAVING AIRPLANE |
| --- |
| Parking Brake | SET |
| Avionic Master Switch | OFF |
| Mixture | IDLE CUT OFF |
| Ignition | OFF |
| Master Switch | OFF |
| Ignition Switch | OFF/REMOVED |
| All Electrical Switches | OFF |
| Cowl Flaps | CLOSED |
| Flight Controls | LOCKED |
| Wheels | CHOCKED |

| AFTER LANDING |
| --- |
| Transponder | SBY/GND |
| Landing /Taxi /Strobe Light | OFF |
| Carb. Heat | COLD |
| Flaps | UP |
| Cowl Flaps | OPEN |

| GO AROUND |
| --- |
| Mixture | RICH |
| Prop Control | HI RPM |
| Throttle | FULL |
| Carb. Head | COLD |
| Climb Speed | 70 MPH |
| Flaps | Up |
| Cowl Flaps | OPEN |

| FINAL |
| --- |
| Autopilot (AP) | OFF |
| Landing Flaps 20°-40° | SET |
| Speed | 70-80 MPH |

| APPROACH |
| --- |
| Speed | 80-90 MPH |
| Landing Light | ON |
| Carburetor Heat | AS REQUIRED |
| Proplever | HIGH RPM |
| Mixture | RICH |
| Flaps | 10° |
| Cowl Flaps | CLOSED |
| Fuel Selector | BOTH |

| Cruise |
| --- |
| Cruise Power | AS REQUIRED |
| Cowl Flaps | AS REQUIRED |

| CLIMB |
| --- |
| Climb Speed | 100-120 MPH |
| Climb Power | 23 IN, 2450 RPM |
| Cowl Flaps | OPEN |

| AFTER TAKE OFF |
| --- |
| Climb Speed | 88/ 100-120 MPH |
| Landing Light | OFF |
| Taxi Light | OFF |
| Climb Power | 23 IN, 2450 RPM |
| Cowl Flaps | OPEN |
| Engine Instruments | GREEN RANGE |
| Flaps | UP |

| BEFORE TAKE OFF |
| --- |
| Directional Gyro | SET |
| Altimeter | hPA/ELEV CKD |
| Ignition Switch | BOTH |
| Carburetor Heat | COLD |
| Proplever | HIGH RPM |
| Mixture | RICH |
| Flaps | UP/20° |
| Cowl Flaps | OPEN |
| Flight Controls | FREE |
| Parking Brake | LOOSE |

| Normal Checklist 182 Back | D-EDJW | EDAN | 02/12 |
| --- | --- | --- | --- |

| SPEED´S (MPH) |
| --- |
| IAS CAS |
| VR NLG LIFT | 60 |
| VX Best Angle Climb | 70 |
| VY Best Rate Climb | 88 |
| V Enroute Climb | 100-120 |
| V Best Glide | 80 |
| V Approach Flaps Up | 80 83 |
| V Approach 20ˆ-40ˆ | 70 75 |
| Vs0 Stall Flaps Up | 64 |
| V Stall Flaps 20ˆ | 40 57 |
| Vs1 Stall Flaps 40° | 55 |